## Slide 1: Affinitizing guest flows
Thilak Raj Surendra Babu

## Slide 2: Problem statement
With higher-density NICS single RX queue will not be sufficient.
VM can have the memory backed in any of the NUMA.
VMs can have a single RX-queue.
RSS could place the Guest flow on a non-optimal queue leading to the below bottlenecks.
  Spin lock contentions amongst PMD threads when different flows belonging to the same VM are serviced by two different threads
  Remote NUMA access due to the flow being serviced by a PMD thread that is from a different NUMA than the VM.
VM1
VM2
VM1-FLOW
VM2-FLOW
PMD-Threads
RSS
NUMA-0
NUMA-1
Figure 1
NIC
Spin Lock
Spin Lock
Cross Numa

## Slide 3: Solution
Having all the flows destined towards a VM placed on the same RXQ will avoid spinlock contention.
Steering the flows towards the PMD thread on the same NUMA as the guest would avoid cross-NUMA access.
Optimize PMD’s mempool access by providing mempool based on the NUMA on which the PMD is running instead of the NUMA on which the interface is attached.
VM1
VM2
VM1-FLOW
VM2-FLOW
PMD-Threads
flow steering based on guest attributes
NUMA-0
NUMA-1
NIC
Workflow:
Hypervisor is multi-NUMA node and has mutli-queue enabled for the physical interface.
On a VM being provisioned use the Guest MAC address and VM’s backing memory to place a steering rule.
  ovs-vsctl set interface enp59s0f1 options:rxq-steer-params=“0|00:00:00:00:00:01,1|00:00:00:00:00:02“

## Slide 4: Tests/Results/Analysis
 | Spin lock | Remote Numa Access
Master | Yes | NUMA 0 and NUMA 1
Rxq_steer | NO | NUMA1
RXQ_steer with Local Mempool | NO | No Significant Remote DRAM access
VM1
VM2
VM1-FLOW
VM2-FLOW
PMD-Threads
Connect –X4
NUMA-0
NUMA-1
PKTGEN-DPDK
flows 2 Entropy at DST MAC
4k Entropy at SRC/DST port
Chart: PPS Vs Pkt Size'
| 64 | 128 | 256 | 512 | 1024 | 1280 | 1500
Master | 3723392 | 3349311 | 2978737 | 2307674 | 1674622 | 1488293 | 1488320
RXQ steering | 5089020 | 4468091 | 3910592 | 2978752 | 2233984 | 2046789 | 1861696
RXQ steering and local pktpool | 4838720 | 4656320 | 3910631 | 3162675 | 2419328 | 2234096 | 2046736
4 PMD threads,
2 on each NUMA,
On Each NUMA one servicing the physical Interface RXQ and other servicing vhostuser

## Slide 5: Possible Applications
Better performance due to lower contention and better NUMA aware placement.
Providing Isolation for a particular guest.

## Slide 6: Thank you
[ovs-dev,RFC] netdev-dpdk: add mac based rxq steering option - Patchwork (ozlabs.org)

## Slide 7: Analysis

## Slide 8: Analysis

## Slide 9: Analysis